## Slide 1: Making Informed Predictions of Pavement Life and Life-Cycle Emissions
How Carbon Budgets for Pavement Maintenance might evolve..
Allan Ogwang

## Slide 2: Literature review
The outlook of pavement management decisions have been purely economic; as the user costs tend to increase with the deterioration of road condition. NCHRP Report (2012), Washington DOT Report (2010)
Lutsey and Sperling, 2009 expounds on importance of pavement in GWP for Transportation sector
Santero and Horvath 2009, Sathaye et al. 2010, Lidicker et.al 2013. Incorporation of GHGs emissions as part of the pavement management decision policy criteria in the transportation sector

## Slide 3: Motivation
IPCC; not more than I trillion tons of Carbon can be released to end of century to maintain the warming below 3.6oF
[by 2011, 469 billion tons of the carbon budget left till the end of the century. ]
Transportation emissions contribute 14% of the global emissions and 28% in the US [EPA, 2014]
California AB32, emissions budget not unprecedented.

## Slide 4: Motivation

## Slide 5: Pavement Management
Source: Franklin Pavement Management, LLC. <http://www.franklinpavement.com/pavement-management.html>

## Slide 6: Pavement Mgt
Source: Agile Assets, “Pavement Management, an Important Validation of the Pavement Performance Concept”

## Slide 7: Pavement Distresses
Cracking
Rutting
Roughness

## Slide 8: Asphalt Pavement Preservation Treatments
Crack seal
Thin Overlay
Slurry Seal
Chip Seal

## Slide 9: Why care?
Source: Hao Wang, “Life Cycel Assessment of Asphalt Pavement Preservation.”

## Slide 10: Case Study: Washington State PMS
State legislature has established the ‘Pavement Preservation Program’
  WSDOT plans for preservation of road network based on rehabilitation needs (resurfacings) for short and long term (10 years).
Three basic pavement types:
  Asphalt (resurfacings frequency: 11-17 yrs)
  Chip seal (6-8 years)
  Concrete Pavement (50 years)
Notes: The mission of the Preservation Program is: “To maintain, preserve, and extend the life and utility of prior investments in transportation systems and services.” (RCW 47.04.280).

## Slide 11: WSDOT PMS
What triggers rehabilitation?
  Cracking?
  Rutting?
  Roughness?
Knowledge of the above determines frequency of overlay
Notes: History has shown that the condition indicators that “trigger” rehabilitation are usually the cracking and rutting indices (described in Section 3.1). This is because roughness tends to be a lagging indicator that appears later because the road was not rehabilitated when it was Due.

## Slide 12: Pavement Distress Evolution
(Nakat and Madanat, 2010)

## Slide 13: Methodology: Overview
Minimize the cracking threshold subject to an Emissions Budget
Dataset contains 999 segments selected from WSDOT pavements
Emission categories:
  Agency (resurfacings)
  User emissions
Use crack initiation and Crack progression model

## Slide 14: Methodology

## Slide 15: Preliminary Results
Chart: GWP Vs Cracking Threshold for 10 Year Budget
| 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25
GWP | 226.9326 | 183.8693 | 146.6993 | 121.7403 | 99.12 | 82.8793 | 77.3109 | 70.2969 | 62.4186 | 48.2447 | 41.2683 | 39.4955 | 35.7619 | 27.8792 | 19.9832 | 19.4792 | 13.6854 | 13.3361 | 10.3165 | 9.3284

## Slide 16: Preliminary results
Chart: GWP Vs Cracking Threshold for 10 Year Budget
| 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25
GWP | 226.9326 | 183.8693 | 146.6993 | 121.7403 | 99.12 | 82.8793 | 77.3109 | 70.2969 | 62.4186 | 48.2447 | 41.2683 | 39.4955 | 35.7619 | 27.8792 | 19.9832 | 19.4792 | 13.6854 | 13.3361 | 10.3165 | 9.3284

## Slide 17: Preliminary Results
Chart: Expected Annual Overlays Vs Cracking Threshold
| 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25
 | 979.4933 | 846.7067 | 715.3767 | 624.8333 | 519.6467 | 438.84 | 387.1667 | 340.4767 | 284.3567 | 206.9233 | 190.3633 | 177.56 | 167.21 | 147.9667 | 135.7 | 132.6333 | 115 | 109.6333 | 106.5667 | 96.6
Average resurfacing frequency is 14 years
(WSDOT)

## Slide 18: Overview of Results
Chart: Expected Annual Overlays Vs Cracking Threshold
| 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25
 | 979.4933 | 846.7067 | 715.3767 | 624.8333 | 519.6467 | 438.84 | 387.1667 | 340.4767 | 284.3567 | 206.9233 | 190.3633 | 177.56 | 167.21 | 147.9667 | 135.7 | 132.6333 | 115 | 109.6333 | 106.5667 | 96.6

## Slide 19: Application..

## Slide 20: Application ctnd..

## Slide 21: Implications:
Informed decision making as per GWP of maintenance practices
More realistic predictions of pavement life
Fair assessment of budget requirements
Provides a basis for comparative analysis of worthwhile investments.